## Slide 1: OpenMP 5+ Tutorial
Presenters
Colleen Bertoni (ANL)
Dossay Oryspayev (BNL)
Johannes Doerfert (ANL)
Tom Scogland (LLNL)
Vivek Kale (BNL)
Acknowledgements: Thanks to Helen He, Tim Mattson,
Barbara Chapman, Michael Klemm and many others for
for some slides used in this presentation.
2022 Exascale Computing Project
Virtual Annual Meeting
May 2nd, 2022
2:30 PM ET – 6:00 PM ET
Notes: Add Swaroop as contributor? Or, make tutorial with contributors

## Slide 2: Agenda (Eastern)
2:30 - 3:15pm Introduction and Demo
3:15 - 3:25pm Break
3:25 - 3:45pm Tips from an LLVM OpenMP developer and Q&A
3:45 - 4:00pm Break
4:00 - 4:45pm Guided Demo/ Hands-on Session
4:45 - 5:00pm Break
5:00 - 6:00pm Advance Topics and Q&A
Q&A Throughout the tutorial – feel free to ask questions

## Slide 3: Overall Acknowledgements
For ECP:
This research was supported by the Exascale Computing Project (17-SC-20-SC), a joint project of the U.S. Department of Energy’s Office of Science and National Nuclear Security Administration, responsible for delivering a capable exascale ecosystem, including software, applications, and hardware technology, to support the nation’s exascale computing imperative.
For ALCF:
This research used resources of the Argonne Leadership Computing Facility, which is a DOE Office of Science User Facility supported under Contract DE-AC02-06CH11357.

## Slide 4: Evolution of DOE Leadership Class Systems
Accelerated node
Name | Cori | Theta | Summit | Sierra | Perlmutter | Frontier | Aurora
System peak (PF) | Haswell: 2.81 KNL: 29.5 | 11.69 | 200 | 125 | > 120 | >1500 (1.5 Exaflops) | ≥ 2000 (2 Exaflops)
Peak Power (MW) | 4.2 | 1.7 | 13.3 |  | 6 |  | 
Total system memory | Haswell: 298.5 TB DDR4 KNL: 1.06 PB DDR4 + High Bandwidth Memory | 1475 TB: 843 DDR4 + 70 MCDRAM + 562 SSD | 2.8 PB: DDR4, HBM2, PB persistent, memory | 1.4 PB DDR4, HBM2, PB persistent, memory | 1.92 PB DDR4 + 240 TB HBM |  | > 10 PB
Node performance (TF) | Haswell: 1.178 KNL: 3.046 | 2.66 | >40 |  | > 70 (GPU) > 4 (CPU) |  | > 130
Node Processors | Intel Haswell Intel KNL | Intel KNL | 2 POWER9 6 NVIDIA Volta GPUs | 2 POWER9 4 NVIDIA Volta GPUs | CPU-GPU nodes: AMD EPYC (Milan) 4x NVIDIA A100 GPU | 1 AMD EPYC CPU 4 AMD Radeon Instinct GPU | 2 Intel Xeon ”Sapphire Rapids” scalable CPU, 6 Intel “Ponte Vecchio” GPU
System Size (nodes) | Haswell; 2,388 nodes KNL: 9,688 nodes | 4,392 nodes | ~4600 nodes | 4320 | > 1500 (GPU) > 3000 (CPU) |  | > 9000
System Interconnect | Aries | Aries | Dual Rail EDR-IB | Dual Rail EDR-IB | HPE Slingshot | HPE Slingshot | HPE Slingshot
File System | 28 PB >700 GB/s Lustre | 10 PB 744 GB/s Lustre | 120 PB 1 TB/s GPFS |  | 35 PB All Flash, Lustre | 2-4x performance / capacity of Summit | ≥230 PB, ≥25 TB/s (DAOS)
Approximate year | 2016 | 2016 | 2018 | 2018 | 2021 | 2021-2022 | 2022-2023

## Slide 5: Evolution of DOE Leadership Class Systems
Name | Cori | Theta | Summit | Sierra | Perlmutter | Frontier | Aurora
System peak (PF) | Haswell: 2.81 KNL: 29.5 | 11.69 | 200 | 125 | > 120 | >1500 (1.5 Exaflops) | ≥ 2000 (2 Exaflops)
Peak Power (MW) | 4.2 | 1.7 | 13.3 |  | 6 |  | 
Total system memory | Haswell: 298.5 TB DDR4 KNL: 1.06 PB DDR4 + High Bandwidth Memory | 1475 TB: 843 DDR4 + 70 MCDRAM + 562 SSD | 2.8 PB: DDR4, HBM2, PB persistent, memory | 1.4 PB DDR4, HBM2, PB persistent, memory | 1.92 PB DDR4 + 240 TB HBM |  | > 10 PB
Node performance (TF) | Haswell: 1.178 KNL: 3.046 | 2.66 | >40 |  | > 70 (GPU) > 4 (CPU) |  | > 130
Node Processors | Intel Haswell Intel KNL | Intel KNL | 2 POWER9 6 NVIDIA Volta GPUs | 2 POWER9 4 NVIDIA Volta GPUs | CPU-GPU nodes: AMD EPYC (Milan) 4x NVIDIA A100 GPU | 1 AMD EPYC CPU 4 AMD Radeon Instinct GPU | 2 Intel Xeon ”Sapphire Rapids” scalable CPU, 6 Intel “Ponte Vecchio” GPU
System Size (nodes) | Haswell; 2,388 nodes KNL: 9,688 nodes | 4,392 nodes | ~4600 nodes | 4320 | > 1500 (GPU) > 3000 (CPU) |  | > 9000
System Interconnect | Aries | Aries | Dual Rail EDR-IB | Dual Rail EDR-IB | HPE Slingshot | HPE Slingshot | HPE Slingshot
File System | 28 PB >700 GB/s Lustre | 10 PB 744 GB/s Lustre | 120 PB 1 TB/s GPFS |  | 35 PB All Flash, Lustre | 2-4x performance / capacity of Summit | ≥230 PB, ≥25 TB/s (DAOS)
Approximate year | 2016 | 2016 | 2018 | 2018 | 2021 | 2021-2022 | 2022-2023
Accelerated node

## Slide 6: OpenMP and the OpenMP Architecture Review Board
The mission of the OpenMP ARB (Architecture Review Board) is to standardize directive-based multi-language high-level parallelism that is performant, productive and portable.

## Slide 7: History of OpenMP: 1997 - 2022
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
In spring, 7 vendors and the DOE agree on the spelling of parallel loops and form the OpenMP ARB. By October, version 1.0 of the OpenMP specification for Fortran is released.
1.0
Minor modifications
1.1
cOMPunity, the group of OpenMP users, is formed to enable researcher participation.and organize workshops
2.0
C/C++ v 1.0. First hybrid applications with MPI* and OpenMP appear.
1.0
The merge of Fortran and C/C+ specifications begins.
2.0
Unified Fortran and C/C++: Bigger than both individual specifications combined.
2.5
Incorporates task parallelism. The OpenMP memory model is defined and codified.
3.0
Support min/max reductions in C/C++.
3.1
Supports offloading execution to accelerator and coprocessor devices, SIMD parallelism, and more. Expands OpenMP beyond traditional boundaries.
4.0
OpenMP supports taskloops, task priorities, doacross loops, and hints for locks. Offloading now supports asynchronous execution and dependencies to host execution.
4.5
2016
2017
2018
Supports: Memory Management API, Reverse Offload, Loop construct, Detached tasks, Custom Mappers,
Tools API
5.0
2019
2020
loop transformation (tiling, ...),
Improved `omp loop`*, variant overloading, runtime variant selection*, compiler agnostic "built-in assume"
5.0
5.1
Permanent ARB
Auxiliary ARB
2021
Specification clarifications
5.2
2022
Locality, loop transformations, clarifications
6.0

## Slide 8: Relevance of OpenMP in ECP
OpenMP is about 50%, out of all choices of X
Update late 2016: 75% of codes use OpenMP
Target directives (to support accelerators): target regions (structured and unstructured), nested target regions, pipelined parallelism, loop transformations, data mapping APIs
Programming memories (High Bandwidth, Low Latency, Accelerator memories) with traits (pinned memory, etc)
Optimization of complex data structure motion (e.g., deep copy)
Improved C++/object-oriented programming support
Improved tasking support: data-locality-aware scheduling, futures, Taskloops, groups, dependences, priorities, cancellation, do across (wavefront parallelism), Ordered (do across), Thread affinity (better control of thread bindings) per parallel region (including nested parallelism)
Asynchronous execution (nowait) and data dependences (depend)
SIMD directives (to support SIMD parallelism)
Focus on continuity of technology and early access to ECP users
NWCHEM
E3SM
CANDLE
LQCD

## Slide 9: OpenMP (Offload) Compilers
Generally about CPU and GPU compilers:
https://www.openmp.org/resources/openmp-compilers-tools/
GPU | Vendor | Compiler | flags
Nvidia | LLVM​ | clang++ | -fopenmp -fopenmp-targets=nvptx64-nvidia-cuda
 | HPE | CC/ftn | -fopenmp -fopenmp-targets=nvptx64/-h omp
 | Nvidia​ | nvc++/ nvfortran | -mp=gpu
 | IBM​ | xlC_r/xlf90_r | -qsmp=omp -qoffload
 | GNU | g++/gfortran | -fopenmp -foffload=-lm
Intel | Intel | icpx/ifx | -fiopenmp -fopenmp-targets=spir64
AMD | AMD | clang++/flang | -fopenmp -fopenmp-targets=amdgcn-amd-amdhsa -Xopenmp-target=amdgcn-amd-amdhsa
 | LLVM | clang++/flang | -fopenmp -fopenmp-targets=amdgcn-amd-amdhsa -Xopenmp-target=amdgcn-amd-amdhsa
 | HPE | CC/ftn | -fopenmp -fopenmp-targets=amdgcn-amd-amdhsa -Xopenmp-target=amdgcn-amd-amdhsa/-h omp
 | GNU | g++/gfortran | -fopenmp -foffload=-lm

## Slide 10: Other OpenMP-relevant Sessions at the ECP Annual Meeting
Early Experience of Application Developers with OpenMP Offloading
  Wed. May 4, 2022
  4:00 PM - 6:00 PM ET / 3:00 PM - 5:00 PM CT / 1:00 PM - 4:00 PM PT
At ECP Annual Meeting Community BoF Days:
  OpenMP Roadmap for Accelerators Across DOE Pre-Exascale/Exascale Machines
    Wed. May 11, 2022
    11:00 AM - 12:30 PM ET / 10:00 AM - 11:30 AM CT / 8:00 AM - 9:30 AM PT
  LLVM in ECP - State of the Union
    Thurs. May 12, 2022
    1:00 PM - 2:30 PM ET / 12:00 PM - 1:30 PM CT / 10:00 AM - 11:30 AM PT

## Slide 11: Important Features in OpenMP
Target directives (support for accelerators)
    structured and unstructured target data regions
    Asynchronous execution (nowait) and data dependences (depend)
Tasking directives (support asynchronous programming)
    Load balancing computation
    Orchestrate work between multicores and accelerators
    Multi-level parallelism
    Taskloops
Loop directives for worksharing (to support multi-cores and accelerators)
SIMD directives (to support SIMD parallelism)
Thread affinity (better control of thread/core bindings)
    Per parallel region (including nested parallelism)
Extended runtime APIs
  Device Memory Routines

## Slide 12: OpenMP – Simple and Modern
Basic Offloading topics
Offloading code to the device
Expressing parallelism
Mapping data

## Slide 13: How to use modern OpenMP – Execution Mapping
GPU
(device)
CPU (host)
move data & issue execution
The target construct offloads the enclosed code to the accelerator: single thread on a device (GPU)

## Slide 14: How to use modern OpenMP – Execution Mapping
The target construct offloads the enclosed code to the accelerator: single thread on a device (GPU)
GPU
CPU (host)
GPU
SM

## Slide 15: How to use modern OpenMP – Execution Mapping
The target construct offloads the enclosed code to the accelerator: single thread on a device (GPU)
The teams construct creates a league of teams: one thread each, concurrent (not parallel) execution (on SMs)
GPU
CPU (host)
GPU
SM

## Slide 16: How to use modern OpenMP – Execution Mapping
The target construct offloads the enclosed code to the accelerator: single thread on a device (GPU)
The teams construct creates a league of teams: one thread each, concurrent (not parallel) execution (on SMs)
The parallel construct creates a new team of threads: parallel execution (by hardware threads)
GPU
CPU (host)
GPU
SM
threads (aka. work items or SIMD lanes)

## Slide 17: How to use modern OpenMP – Execution Mapping
The target construct offloads the enclosed code to the accelerator: single thread on a device (GPU)
The teams construct creates a league of teams: one thread each, concurrent (not parallel) execution (on SMs)
The parallel construct creates a new team of threads: parallel execution (by hardware threads)
The simd construct indicates SIMD execution is allowed
GPU
CPU (host)
GPU
threads (aka. work items or SIMD lanes)
SM

## Slide 18
Coarse-grained parallelism
  Teams
    GPU SMs* (not 1-1 mapping)
Fine-grained parallelism
  Parallel [+SIMD]
    Cuda cores in an SM*
* For NVIDIA GPUs
How to use modern OpenMP – Execution Mapping

## Slide 19: How to use OpenMP – Execution Example
The target construct offloads the enclosed code to the accelerator
The teams construct creates a league of teams
The distribute construct distributes the outer loop iterations between the league of teams
The parallel for combined construct creates a thread team for each team and distributes the inner loop iterations to threads
#pragma omp target
#pragma omp teams distribute
for (i=0; i<N; ++i) {
#pragma omp parallel for
for (j=0; j<N; ++j) {
x[j+N*i] *= 2.0;
}
}

## Slide 20: How to use OpenMP – Data Mapping Example
#pragma omp target map(tofrom:x[0:M])
#pragma omp teams distribute
for (i=0; i<N; ++i) {
#pragma omp parallel for
for (j=0; j<N; ++j) {
x[j+N*i] *= 2.0;
}
}
The target construct offloads the enclosed code to the accelerator
The teams construct creates a league of teams
The distribute construct distributes the outer loop iterations between the league of teams
The parallel for combined construct creates a thread team for each team and distributes the inner loop iterations to threads
The map construct maps data for a single target region

## Slide 21: How to use OpenMP – Data Mapping Example
The target construct offloads the enclosed code to the accelerator
The teams construct creates a league of teams
The distribute construct distributes the outer loop iterations between the league of teams
The parallel for combined construct creates a thread team for each team and distributes the inner loop iterations to threads
The map construct on a target region maps data for that target region
#pragma omp target enter data map(tofrom: x[0:M])
#pragma omp target exit data \
map(from:x[0:M])
#pragma omp target
#pragma omp teams distribute
for (i=0; i<N; ++i) {
#pragma omp parallel for
for (j=0; j<N; ++j) {
x[j+N*i] *= 2.0;
}
}

## Slide 22: OpenMP Device Constructs – core functionality
Execute code on a target device
  omp target [clause[[,] clause],…]
  structured-block
  omp declare target
  [function-definitions-or-declarations]
Manage the device data environment
  map ([map-type:] list)
  map-type := alloc | tofrom | to | from | release | delete
  omp target data [clause[[,] clause], …]
  structured-block
  omp target enter/exit data [clause[[,] clause], …]
  omp target update [clause[[,] clause],…]
  omp declare target
  [variable-definitions-or-declarations]
Parallelism & Workshare for devices
  omp teams [clause[[,] clause],…]
  structured-block
  omp distribute [clause[[,] clause],…]
  for-loops
Device Runtime Routines
  void omp_set_default_device(int dev_num)
  int omp_get_default_device(void)
  int omp_get _num_devices(void)
  int omp_get_team_num(void)
  int omp_is_initial_device(void)
  …
Environment variables
  OMP_DEFAULT_DEVICE
  OMP_THREAD_LIMIT

## Slide 23: Demo
OpenMP Offload 101
Offloading code to the device and getting device info
Expressing parallelism
Mapping data
Details and slides: https://anl.box.com/v/openmp-tutorial-2022
# pull from github
$ git clone https://github.com/vlkale/OpenMP-tutorial
$ cd OpenMP-tutorial/offload-101

## Slide 24: Resources for OpenMP
OpenMP Specifications and OpenMP Examples (ratified by OpenMP Language Committee) can be found at: https://www.openmp.org/specifications/
Compilers that support OpenMP:
  https://www.openmp.org/resources/openmp-compilers-tools/#compilers
Test-suites:
  SOLLVE V&V: Test-suite for all the new features introduced in OpenMP 4.5+ with focus on features important for ECP applications [ https://github.com/SOLLVE/sollve_vv ]
  OvO: It is a collection of OpenMP Offloading test functions for C++ and Fortran [ https://github.com/TApplencourt/OvO ]
  OpenMP IBM Tests: OpenMP Volta GPU tests [ https://github.com/clang-ykt/omptests ]